## Slide 1
Wireless Open Access Research Platform (WARP)
FPGA Team (GSSST H/W LAB)
Under The Guidance of
Dr. Suvra Sekhar Das
G. S. Sanyal School of Telecommunication
Indian Institute of Technology, Kharagpur
Oct 7th, 2013

## Slide 2
  WARP V2 (Virtex-IV) Board
FPGA Power
Supply
External Power
Supply
Multi Gigabit Transceiver
(MGT)
Ethernet
Radio Card
Virtex-4 FPGA
Clock Baord

## Slide 3
WARP FPGA BOARD
Rice University’s Wireless Open-Access Research Platform (WARP)
C programmable interrupt driven embedded system
Uses Xilinx’s Virtex IV FPGA for processing and storage
Radio boards can be used as transceiver, can operate at either 2.4 GHz or 5 GHz (ISM band) with 40 MHz bandwidth
Versions of WARP Hardware:
  WARP V1(Virtex-II pro)
  WARP V2(Virtex-IV)
  WARP V3(Virtex-VI)

## Slide 4
WARP FPGA Board Power Supplies
Required External Supply:
The WARP FPGA board operates from a single external 12v supply. This supply is generally connected to the board's coaxial power connector.
FPGA Power Supplies
The Virtex-4 FPGA has a number of different power inputs. The table below summarizes the power supplies on the WARP FPGA board.
Supply | Voltage | Description
VCC_EXT | 12v | External supply
VCC_5 | 5.0v | Daughter card slot supply
VCC_INT | 1.2v | FPGA core logic
VCC_AUX | 2.5v | FPGA clock resources
VCC_O | 3.3v, 2.5v & 1.8v | FPGA I/O banks
MGT_x | 2.5v, 1.5v & 1.2v | MGT logic and I/O
VCC_0.9 | 0.9v | DDR2 SO-DIMM termination

## Slide 5
WARP FPGA Board Daughtercard Slots
The WARP FPGA Board has four daughtercard slots. The four slots are electrically and mechanically identical. The WARP hardware supports any combination of daughtercards in the four slots.

## Slide 6
WARP FPGA Board User I/O’s
Push Buttons
LEDs
Hex Displays

## Slide 7
WARP FPGA Board Ethernet and other I/O’s
Ethernet:
The FPGA Board has one 10/100/1000 Mbps Ethernet device present. Virtex-4 FPGA uses one of the hardened Tri-mode Ethernet MAC for the MAC layer.
USB-UART:
The FPGA board includes a USB-UART interface, You can connect this port to a PC via a standard USB cable
RS232-UART:
The FPGA board also includes a standard RS-232 serial port. The board's female DB9 port is configured just like a PC, with Tx on pin 3, Rx on pin 2 and GND on pin 5.
DIGITAL I/O’s:
There are 16-bits of unbuffered 3.3v I/O connected directly to FPGA I/O pins

## Slide 8
WARP Radio Board
LED’s
DIP Switches
RF Transceiver
MAX 2829
Dual D/A
Converters
AD9777
A/D Converter
AD9200
Dual A/D
Converters
AD9248-65

## Slide 9
WARP Clock Board

## Slide 10
WARP Analog Board

## Slide 11
-> initialize
-> send Binary Data
-> start tx/rx
<- read Binary Data
Ethernet
  OFDM Transceiver Over The Air Demo FPGA / HW
MATLAB
User Application
WARPLab Framework
Host Computer
FPGA
Analog
Radio 3
Radio 2
Radio 1
Ethernet
WARP Node
Error correction coding | Error Correction Decoding
Symbol Mapping | Symbol De-mapping
OFDM modulation via IFFT | OFDM Demodulation via IFFT
CP | CP & Time synchronization
I/Q Tx | I/Q Rx
DAC | ADC
Up-conversion RF Tx Front end | RF Rx Down conversion
Transmitter | Receiver
Input binary data | Output binary data
Hardware Design Flow
Xilinx ISE
EDK
(Bitstream
Out)
Xilinx ISE
System Generator
Custom design
*.m (Matlab)
*.mdl(Simulink)
*.c/c++
pcore
WARP
pcore device driver
Custom bitstream
24th July 2012
Delhi

## Slide 12: Expemintal Set Up (FPGA based OFDM Test Bed)
Application
Warp Board
Oscilloscope
Antennas

## Slide 13: OFDM Symbol output Hardware
OFDM Symbol in Hardware
I,Q Constellation output in Hardware

## Slide 14: Expemintal Set Up (RRA and Co-ordinated scheduling)

## Slide 15: Expemintal Set Up (MIMO)
WARP Board
Control
Application
Antennas
MIMO
Demonstration
(WARPLAB)
Ethernet
Switch

## Slide 16
THANK YOU